## Slide 1
Wildfire Level-Set Solver
AMReX-Powered Wildfire Spread Simulation
Level-Set / FARSITE
Rothermel · Balbi · Cheney-Gould
Crown Fire & Spotting
Mass-Consistent Wind
AMReX MLMG
github.com/hgopalan/wildfire_levelset

## Slide 2
Architecture
INPUTS
• Terrain / DEM (X Y Z)
• Landscape file (.lcp)
• Fuel model (FBFM13/40)
• Weather & wind field
• Ignition geometry
CORE ENGINE
Fire Spread
Rothermel · Balbi · Cheney-Gould
Propagation
Level-Set (WENO5+RK3) · FARSITE
Crown Fire
Van Wagner criterion
Spotting
Stochastic · Albini physics
Wind
Mass-consistent MLMG Poisson
OUTPUTS
• AMReX plotfiles
• Fire perimeter CSV / GeoJSON
• Intensity & flame length
• Wind field (u v w)
• Terrain-aligned CSV

## Slide 3
Fire Spread Physics
Rothermel 1972
Surface fire rate-of-spread Fuel loading · moisture · wind Slope correction
Balbi 2009
Radiative-convective physics Flame tilt & depth coupling Live / dead fuel
Cheney-Gould
Grass fire empirical model Curing fraction effect Fast-running surrogate
Propagation
Level-Set (WENO5-Z + RK3)
FARSITE Elliptical Huygens
Anderson Dynamic L/W Ratio

## Slide 4
Sub-Models & Physics
👑 Crown Fire
Van Wagner (1977) CBH · CBD · FMC thresholds Torching initiation
🔥 Spotting — Stochastic
Firebrand generation Lognormal / Exponential distance distribution
🌊 Spotting — Albini
Thermal-plume lofting 2-D trajectory integration Physics-based range
📊 Fuel Consumption
Post-frontal burnout Residence-time model Bulk fraction depleted
🌡 Fire Diagnostics
Byram fireline intensity Flame length at every step CSV / GeoJSON perimeter
💨 Wind Adjustment
Wind Adjustment Factor Max effective wind limit Andrews (2018)

## Slide 5
Terrain-Following Wind Solver
1 Read terrain
X Y Z point cloud → IDW interpolation
2 Log-law profile
u(z_agl) = (u*/κ) ln((z + z₀)/z₀)
3 Poisson solve
AMReX MLMG · MLABecLaplacian · level-0
4 Mass-consistent u
u = u₀ − α_h² ∇_h λ w = w₀ − α_v² ∂λ/∂z
5 Extract & output
Plotfile + terrain-aligned CSV slice
Key Features
✦ Stand-alone executable (wind_solver)
✦ Anisotropic Poisson: α_h ≠ α_v
✦ QUIC-URB style Lagrange multiplier
✦ dx / dy / dz user-specified (default 30 m)
✦ Vertical domain: 0 → 300 m
✦ Always 3-D, even in 2-D levelset builds
✦ Terrain-aligned CSV extraction (extract_agl)
✦ MPI + GPU portable (AMReX backend)

## Slide 6
Terrain-Aligned Wind Extraction
Terrain surface z_s(x, y)
Extraction surface z_physical = z_terrain + z_agl
z_agl (const.)
ParmParse Options
# By AGL height (metres): extract_agl = 15.0 # By k-index: extract_k = 0 # Output file: extract_file = wind_extract.csv
CSV Columns
x · y · z_terrain z_physical · z_agl u · v · w · speed

## Slide 7
Fuel Models & Landscape
Anderson 13 (FBFM13)
FM1 – FM13 standard fuel classes • Short grass · Timber litter • Chaparral · Slash • Per-class moisture (1hr/10hr/100hr, live herbaceous, live woody) Wind Adjustment Factor (WAF) Max Effective Wind Speed (MEWS)
Scott & Burgan 40 (FBFM40)
GR · GS · SH · TU · TL · SB classes • Grass · Grass-Shrub • Shrub · Timber Understory • Timber Litter · Slash-Blowdown LANDFIRE landscape file (.lcp) support Per-cell spatial fuel variation

## Slide 8
HPC Backend — AMReX
Block-Structured AMR
Adaptive mesh refinement Focus resolution on fire front
MPI Parallelism
Domain decomposition Scales to HPC clusters
GPU Acceleration
CUDA · HIP · SYCL backends AMReX GPU-portable kernels
MLMG Linear Solver
Multilevel multigrid MLABecLaplacian for wind Poisson
2D / 3D Flexible
2-D for fast runs 3-D for full terrain physics
Embedded Boundaries
Complex geometry EB-aware stencils

## Slide 9
Regression Tests
basic_levelset
farsite_ellipse
rothermel_fuel
terrain_wind
crown_fire
albini_spotting
eb_implicit
landfire_farsite
gaussian_hill_wind_solver ★
ctest -L regtest · ctest -L wind_solver · ctest -R gaussian_hill_wind_solver
★ new wind_solver regtest

## Slide 10
Python Tools
srtm_terrain_reader.py
Download & process SRTM DEM → terrain.csv
wrf_wind_reader.py
Extract WRF wind field → velocity CSV
plotfile_to_geotiff.py
AMReX plotfile → GeoTIFF (GIS ready)
farsite_fmd_reader.py
Parse FARSITE .fmd fuel moisture schedule
farsite_fms_reader.py
Read FARSITE .fms weather stream
landscape_writer.py
Write FARSITE .lcp landscape files
utm_convert.py
UTM ↔ lat/lon coordinate conversion
generate_terrain.py ★
Generate Gaussian hill terrain for regtest
★ new in this release

## Slide 11
Quick Start
1
Clone
git clone --recurse-submodules https://github.com/hgopalan/wildfire_levelset.git
2
Build
cmake -S . -B build cmake --build build -j
3
Run levelset
cd regtest/basic_levelset ../../build/levelset inputs.i
4
Run wind solver
cd regtest/gaussian_hill_wind_solver ../../build/wind_solver inputs.i
5
Run all tests
cd build && ctest -L regtest --output-on-failure
cmake -DLEVELSET_BUILD_WIND_SOLVER=ON (default ON, always 3-D)
cmake -DLEVELSET_DIM_2D=ON → wind_solver built as separate 3-D ExternalProject

## Slide 12
Summary
🔥 3 fire spread models
Rothermel · Balbi · Cheney-Gould
🌲 Full crown & spotting physics
Van Wagner + Albini + stochastic
💨 Mass-consistent wind solver
QUIC-URB style · MLMG Poisson
🗺 Terrain-aligned extraction
Constant AGL CSV slice over complex terrain
⚡ GPU-ready HPC framework
AMReX · CUDA · HIP · SYCL · MPI
✅ Comprehensive regression suite
9 regtests · CTest integration
github.com/hgopalan/wildfire_levelset