## Slide 1
Wildfire-AMR
An AMReX-based level-set solver for wildfire front propagation
Rothermel · FARSITE · Balbi · Crown Fire · Firebrand Spotting
Fuel Adjustment · Time-Varying Moisture · Spatial Crown Layers · Perimeter Output
GPU-Accelerated (CUDA / HIP / SYCL) · MPI-Parallel · Embedded Boundaries
github.com/hgopalan/wildfire_levelset
⚠ AI-assisted research code — validate before operational use

## Slide 2
Motivation
Why a new level-set wildfire solver?
The Problem
🔥 Wildfire area in the US exceeded 10 M acres in recent years
🔥 Climate change is extending fire seasons globally
🔥 Operational tools (FARSITE, FlamMap) are serial CPU codes
🔥 WRF-SFIRE couples fire to atmosphere but is complex to run
🔥 Research needs fast, open, GPU-ready experimentation platform
Our Approach
✔ Open-source AMReX framework (LBNL) for structured meshes
✔ Level-set method: robust, implicit fire front representation
✔ Plug-in fire spread models: Rothermel, Balbi, Cheney-Gould
✔ FARSITE elliptical expansion on an Eulerian grid
✔ GPU kernels via AMReX ParallelFor (CUDA/HIP/SYCL)
Key Differentiators
★ Fully open-source (GitHub)
★ Supports real LANDFIRE landscape files (.lcp)
★ GIS output: GeoTIFF, GeoJSON, CSV perimeters
★ Compatible with WRF/WindNinja wind fields
★ Regression-tested, documented, benchmarked

## Slide 3
Repository Structure
src/ C++ solver source (all models, I/O, main loop)
main.cpp AMReX setup, time loop, plotfile writes
rothermel_model.H Rothermel (1972) ROS + Andrews (2018) adjustments
farsite_ellipse.H Richards (1990) FARSITE elliptical expansion
balbi_model.H Balbi (2009) physical fire spread
lcp_binary_reader.H Binary FARSITE LCP reader (new)
fuel_adjustment.H .adj fuel adjustment file reader (new)
fuel_moisture_scheduler.H Time-varying .fmd moisture (new)
scott_spotting_table.H Max spotting distance table (new)
write_xy_data.H Perimeter CSV/GeoJSON + stats CSV (new)
tools/ Python pre/post-processing utilities
regtest/ Regression tests (CTest / CMake)
docs/ Sphinx documentation
external/ AMReX submodule

## Slide 4
Level-Set Method for Fire Front Tracking
Hamilton-Jacobi PDE on a fixed Eulerian grid
Level-Set Formulation
● Fire front = zero-contour of signed distance function φ(x,t)
● φ < 0 inside burned region; φ > 0 outside (unburned)
● Front advances via: ∂φ/∂t + F|∇φ| = 0 (F = ROS)
● WENO5Z spatial scheme + 3rd-order TVD Runge-Kutta in time
● Periodic reinitialization restores signed-distance property
● Supports both pure level-set and FARSITE ellipse propagation
Level-set PDE / FARSITE speed function
∂φ/∂t + F|∇φ| = 0 F(x,t) = R(x,t) = Rothermel / Balbi / FARSITE ROS F_FARSITE(θ) = a / (1 − b·cos(θ − θ_wind)) a = (R_head + R_back)/2 b = (R_head − R_back)/(R_head + R_back)
Signed-distance reinitialization
Reinitialization PDE: ∂φ/∂τ + sign(φ₀)(|∇φ| − 1) = 0 advanced to steady state (|∇φ| → 1) using WENO5Z + RK3 in pseudo-time τ
Numerics
● WENO5Z (Borges 2008): 5th-order upwind, low dissipation
● TVD-RK3 (Shu-Osher): 3rd-order, total-variation stable
● Adaptive dt from CFL condition: dt = CFL·dx/max(F)
● Ghost-cell / extrap. BCs at domain boundaries

## Slide 5
Rothermel (1972) Fire Spread Model
Semi-empirical surface fire ROS — the core of FARSITE and FlamMap
Rothermel ROS equation
R = I_R · ξ · (1 + φ_w + φ_s) / (ρ_b · ε · Q_ig) I_R = Γ' · w_n · h · η_M · η_s [reaction intensity, kW/m²] ξ = exp(0.792 + 0.681·σ^0.5 · (β+0.1)) / (192 + 0.259·σ) φ_w = C · (U / (β·β_op)^E)^B [wind factor] φ_s = 5.275 · β^−0.3 · tan²(θ) [slope factor]
Moisture damping & fuel load
η_M = 1 − 2.59·r_M + 5.11·r_M² − 3.52·r_M³ r_M = M_f / M_x (dead fuel: M_x = 0.12–0.40) Multi-class moisture (1-hr, 10-hr, 100-hr, live herb, live wood): w_n = w₁·(1−S_T) + w₁₀·(1−S_T) + w₁₀₀·(1−S_T) + w_lh·... + w_lw·...
Fuel System
● Anderson 13 models: FM1–FM13
● Scott & Burgan 40 models: GR, GS, SH, TU, TL, SB
● Per-cell fuel from FARSITE landscape file (.lcp)
● Andrews (2018) WAF: 20-ft → midflame wind
● Andrews (2018) MEWS: cap φ_w at 90% of I_R
● Fuel adj. file (.adj): per-model ROS multiplier
● Time-varying moisture (.fmd): hourly update

## Slide 6
FARSITE Elliptical Fire Expansion
Richards (1990) Huygens wavelet — Eulerian level-set implementation
Ellipse Model
● Each fire-front point launches an elliptical wavelet
● Ellipse axes set by R_head, R_back, L/W ratio
● Eulerian implementation: FARSITE spread vector d = (dx, dy) per cell
● Level-set advected by φ_t + d·∇φ = 0
● Anderson (1982) dynamic L/W: L/W = 0.936·exp(0.1147·U) + 0.461
● Alternative shapes: Catchpole-de Mestre, Wilson, Alexander lemniscate
FARSITE ellipse geometry
Ellipse semi-axes: a = (R_head + R_back) / 2 (semi-major) b = a / LW_ratio (semi-minor) c = a − R_back (focus offset) Speed in direction θ (from head): F(θ) = a·(1 − e²) / (1 − e·cos θ) e = c/a (eccentricity)
Spread vector computation
Head ROS: R_head = R_Rothermel(U_wind, slope) Back ROS: R_back = R_head / (LW + (LW²−1)^0.5) FARSITE spread vector per cell (i,j): d_x = F(θ) · cos(θ_wind + θ_slope) d_y = F(θ) · sin(θ_wind + θ_slope)

## Slide 7
Balbi (2009) Physical Fire Spread Model
Radiation-driven, physics-based ROS — replaces Rothermel when fire_spread_model=balbi
Balbi ROS equation
R = A · (1 + sin α − cos α) · exp(B·U_eff·cos α) − B·U_eff·cos α · R₀ A = r·B·[T_f/(T_a − T_f)] · [1 − exp(−B·U_eff·cos α)] B = C_p_f · ρ_f · (1 + δ/h)^(−1) (geometric factor) α = flame tilt angle from vertical U_eff = wind + buoyancy: v_b = √(v_b_fuel² + v_b_Q²)
Flame tilt and buoyancy velocity
tan α = U_eff / v_b (from momentum balance) v_b = √(2g·δ·(T_f−T_a)/T_a) (buoyancy from fuel) v_b_Q = k_upward·√(g·Q·H / (ρ·C_p·T_a)) (from heat flux Q) R₀ = radiant ROS with no wind/slope (Albini 1985)
Usage
● Activated by fire_spread_model = balbi
● Auto-generates per-fuel Balbi parameter table
● Parameters: T_a, T_f, T_i, C_p_f, rho_f, h, r, delta
● Fully compatible with all 6 Viegas wind-terrain options
● Heat flux Q augments buoyancy velocity
● Landscape .lcp fuel model used for per-cell table lookup

## Slide 8
Crown Fire, Firebrand Spotting & Ecology Diagnostics
Crown Fire (Van Wagner 1977)
● Van Wagner (1977) active crown fire criterion:
● I_B ≥ I_B_crit = (0.01·CBD·(CBH/FMC)²)^1.5
● Crown fraction = I_B / I_B_crit (clamped 0–1)
● Per-cell CBH, CBD from binary LCP (use_spatial_crown=1)
● Global fallback: crown.CBH, crown.CBD, crown.FMC
Firebrand Spotting (Albini 1983)
● Albini (1983) 2D trajectory integration:
● z_max = terminal_velocity·√(I_B/(C_d·g·ρ_a))
● Trajectory integrated with RK2 including drag
● Spot activated when φ > 0 at landing cell
● Stochastic model: P_spot ~ P_base·(I_B/I_ref)·f(M_f)
● Scott/Albini table: max distance by fuel model + wind
Fire Behavior Diagnostics
● Byram (1959) fireline intensity: I_B = H·w·R [kW/m]
● Byram flame length: L_f = 0.0775·I_B^0.46 [m]
● Van Wagner scorch height [m]
● Anderson (1970) prob. of sustained ignition
● Ryan-Reinhardt tree mortality fraction
● Crown activity: surface / passive / active
● CO₂, CO, PM₂.₅ emissions [kg/m²]
Fire intensity & spotting distance
I_B = H · Σ(w_i · r_i) · R [kW/m] H = heat content [kJ/kg] w_i = fuel load per class [kg/m²] r_i = consumption fraction Scott/Albini max distance [m] by fuel model: FM4: 1800 m FM10: 1200 m FM13: 1800 m d_scaled = d_base · √(U / 9 m/s)

## Slide 9
Terrain Effects & Wind-Terrain Feedback Models
Slope correction
Rothermel (1972) slope factor: φ_s = 5.275 · β^(−0.3) · tan²(θ_slope) FARSITE aspect correction: rotate wind vector by terrain aspect Per-cell slope & aspect from: 1) Constant values (slope=, aspect=) 2) Terrain XYZ file (rothermel.terrain_file) 3) Binary or ASCII landscape .lcp (rothermel.landscape_file)
wind_terrain.model options
1 – Default No modification; ambient wind drives ROS
2 – Viegas ROS Viegas (2004) exp. slope factor as actual ROS
3 – Viegas wind Buoyancy upslope velocity perturbation (eruptive)
4 – Canyon wind Rothermel (1983) canyon wind amplification
5 – Viegas-Neto Viegas & Neto (1994) buoyancy-driven upslope
6 – Pimont Pimont et al. (2009) exponential slope correction
7 – WindNinja Ridge/canyon empirical speed-up (wind-slope alignment)
Terrain coupling equations
Viegas eruptive criterion: R_V / R₀ = exp(a_V · tan φ) Eruptive when R_V / R₀ > critical ratio WindNinja ridge/canyon: f_ridge = 1 + k_ridge · tanφ · alignment f_canyon = 1 + k_canyon · tanφ · |alignment|
Turbulence & Heat-Flux Wind
● Turbulent wind: Ornstein-Uhlenbeck process
● σ = amplitude, θ = decorrelation rate
● Options: OU, Gaussian spatial corr., RFF spectral, direction walk
● Heat flux: fire plume buoyancy (upward + inflow)

## Slide 10
New Features (2025)
Binary LCP · Crown Layers · Fuel Adj · FMD Moisture · Perimeter Output · Spotting Table · Stats CSV
🗺 Binary LCP Reader
Auto-detects binary vs ASCII .lcp format. Reads all layers including crown CBH/CBD/CC. src/lcp_binary_reader.H
🌲 Spatial Crown Layers
Per-cell CBH, CBD, canopy cover from binary LCP. Written to every plotfile as cbh/cbd/canopy_cover. use_spatial_crown = 1 (default)
⚙ Fuel Adjustment (.adj)
Per-fuel-model ROS multipliers at startup. fuel_adj_file = fire.adj tools/farsite_adj_reader.py
💧 Time-Varying Moisture (.fmd)
Hourly moisture schedule; updates every step. fmd_file = schedule.fmd tools/farsite_fmd_reader.py
📍 Perimeter CSV / GeoJSON
Fire front boundary at every plotfile step. write_perimeter_csv = 1 write_perimeter_geojson = 1
📊 Spotting Distance Table
Scott/Albini (1979) max distances by FBFM13/40. Diagnostic printed alongside Albini spotting. src/scott_spotting_table.H
📈 Burned Area Time Series
fire_stats.csv: step, time, area [ha], perimeter [km], front cells, emissions. fire_stats_file = fire_stats.csv

## Slide 11
Key Input Parameters (inputs.i / ParmParse)
Grid / Domain
n_cell_x/y/z = 64
prob_lo/hi_x/y/z = 0 / 1000 [m]
max_grid_size = 64
cfl = 0.5
nsteps or final_time
Fire Spread
fire_spread_model = rothermel|balbi|cheney_gould
propagation_method = levelset|farsite
rothermel.fuel_model = FM4
rothermel.landscape_file = terrain.lcp
rothermel.use_waf = 0|1 (Andrews WAF)
New: Fuel Adj & Moisture
fuel_adj_file = fire.adj
fuel_adj_model = 4 (global model)
fmd_file = schedule.fmd
fmd_start_month/day/hour
fmd_fuel_model = 0 (all models)
New: Perimeter & Stats
write_perimeter_csv = 1
write_perimeter_geojson = 1
fire_stats_file = fire_stats.csv
use_spatial_crown = 1
Crown Fire
crown.enable = 0|1
crown.CBH = 4.0 [m]
crown.CBD = 0.15 [kg/m³]
crown.FMC = 100.0 [%]
use_spatial_crown = 1 (from LCP)
Spotting
spotting.enable = 0|1
albini_spotting.enable = 0|1
albini_spotting.I_B_min = 10.0
albini_spotting.terminal_velocity = 1.0
Scott table printed as diagnostic
Wind-Terrain
wind_terrain.model = none|viegas_ros|canyon_wind|...
turb_wind.model = ou|spectral_noise|...
heat_flux.value = 1000 [W/m²]
u_x / u_y / u_z [m/s]
velocity_file = wind.csv
Output
plot_int = 50
chk_int = -1
viegas.enable = 0|1
weise_biging.enable = 0|1
emissions.EF_CO2 = 1.57 [kg/kg]

## Slide 12
Python Tools (tools/ directory)
farsite_adj_reader.py ★
Inspect / generate / apply FARSITE .adj fuel adjustment files. --adj fire.adj (inspect) --generate --fuel-system 13 (template) --apply-csv params.csv (calibrate)
farsite_fmd_reader.py ★
Parse / convert / query / generate .fmd moisture schedules. --fmd fire.fmd --output sched.csv --query-time 3600 --fuel-model 4 --generate --M-d1 8 --hours 24
landscape_writer.py
Download LANDFIRE rasters → FARSITE .lcp landscape file. --lat-min 40 --lat-max 40.5 --lon-min -105 --lon-max -104.5 Produces landscape.lcp
srtm_terrain_reader.py
Download SRTM1 elevation data → UTM terrain XYZ file. --lat-min 40.0 --lat-max 40.5 --lon-min -105 --lon-max -104.5
wrf_wind_reader.py
Extract U/V wind from a WRF netCDF file → solver wind CSV. --wrf-file wrfout_d01_... --wind wind.csv
farsite_weather_reader.py
Parse FARSITE .wtr RAWS weather files → time-stamped wind CSVs for use_time_dependent_wind.
fuel_moisture_from_weather.py
Estimate equilibrium dead-fuel moisture from temperature and relative humidity (Nelson 1984).
plotfile_to_geotiff.py
Convert AMReX plotfiles → GeoTIFF rasters + GeoJSON fire-perimeter contours. --all --outdir gis_out --utm-origin 450000 4200000
★ New tools added in 2025

## Slide 13
Build, Run & Output
Build
● cmake -S . -B build (3D CPU default)
● cmake -S . -B build -DLEVELSET_DIM_2D=ON
● cmake -S . -B build -DLEVELSET_GPU_BACKEND=CUDA
● cmake -S . -B build -DLEVELSET_ENABLE_MPI=ON
● cmake --build build -j
Run
● ./build/levelset inputs.i
● Or override: u_x=5 cfl=0.4 plot_int=20
● Works with any inputs.i from regtest/
● Restart: restart_chkfile = chk0050
● Checkpoint: chk_int = 50
Output Files
● plt####/ — AMReX plotfile per plot_int step
● phi_negative_NNNN.dat — burned cell centres
● phi_envelope_NNNN.dat — convex hull
● perimeter_NNNN.csv — fire front boundary
● perimeter_NNNN.geojson — GeoJSON Polygon
● fire_stats.csv — area/perimeter time series
Plotfile Variables
● Plotfile variables: phi, velx/y, R, fireline_intensity, flame_length,
● cbh, cbd, canopy_cover (new), elevation, slope, aspect, fuel_model,
● scorch_height, prob_ignition, tree_mortality, crown_activity,
● co2/co/pm25_emissions, arrival_time, heat_per_unit_area, vorticity_z,
● weise_*, viegas_*, spot_*, albini_*
● View with: ParaView, VisIt, or tools/plotfile_to_geotiff.py

## Slide 14
Regression Tests & Timing Benchmark
CTest framework — run with: cd build && ctest -L regtest --output-on-failure
Core Regtests
● basic_levelset — level-set sphere advection
● farsite_ellipse — FARSITE elliptical expansion
● rothermel_fuel — Rothermel + fuel models
● anderson_lw — Anderson dynamic L/W
● cheney_gould_grassfire— Cheney & Gould (1995) grassland
● catchpole_demestre — double-ellipse shape
● wilson_spread — Wilson (1988) ellipse
● alexander_lemniscate — Limaçon fire shape
● landfire_farsite — LANDFIRE landscape (Python3)
New Feature Regtests (2025)
● fuel_adj_file — .adj reader + adjuster
● fmd_moisture — .fmd time-varying moisture
● fire_perimeter_output — CSV+GeoJSON perimeter writers
● fire_perimeter_output_validate — validates output files
● burned_area_timeseries — fire_stats.csv time series
●
● 3d_sphere (3D build only)
● terrain_wind (2D only)
● time_dependent_wind (2D only)
timing_benchmark ★ (CTest label: benchmark)
Multi-resolution wall-clock benchmark: python3 run_benchmark.py --exe ./levelset \ --dim 2 --nsteps 20 \ --resolutions 32 64 128 256 Scenarios: levelset, farsite Checks: monotone runtime, scaling exponent α ∈ [0.8D, 1.6D] Output: timing_results.csv CTest label: benchmark ctest -L benchmark --output-on-failure -V

## Slide 15
Comparison with FARSITE and WRF-SFIRE
Capability
Wildfire-AMR
FARSITE
WRF-SFIRE
Fire spread model
Rothermel+Balbi+C&G +elliptical FARSITE LS
Rothermel+FARSITE
Rothermel (level-set)
Wind coupling
One-way (prescribed)
One-way (prescribed)
Two-way (fire↔atmos)
Terrain
Per-cell LCP: elev, slope, aspect, fuel
Full 2D .lcp
Full 3D WRF grid
Crown layers (spatial)
✔ CBH/CBD/CC from binary LCP
✔ from .lcp
✘ not standard
Fuel adjustment (.adj)
✔ fuel_adj_file
✔ native
✘
Time-varying moisture
✔ .fmd schedule
✔ native .fmd
✔ prescribed
Perimeter CSV/GeoJSON
✔ built-in
✔ shapefiles
NC (WRF output)
GPU acceleration
✔ CUDA/HIP/SYCL
✘
✘
MPI parallelism
✔ AMReX DD
✘
✔ WRF MPI
Embedded boundaries
✔ AMReX EB
✘
✘
Timing benchmark
✔ CTest benchmark label
✘
✘
Open source
✔ (GitHub)
✘ (US FS license)
✔ (WRF license)

## Slide 16
Limitations & Future Roadmap
Current Limitations
⚠ Fuel models: Anderson 13 + Scott & Burgan 40 only; no custom dynamic fuel models
⚠ Fuel moisture: time-varying .fmd works; no transport PDE
⚠ Wind: spatial CSV or WRF; no fully 3D gridded field
⚠ Fire↔atmosphere: one-way by default (wind-terrain feedback available)
⚠ Crown fire: Van Wagner (1977) empirical only; no mechanistic spread model
⚠ Spotting: 2D trajectory; no 3D plume transport
⚠ Validation: limited against real fire events
⚠ Serial I/O paths (landscape, spotting) — GPU kernels for spread
Potential Future Work
→ Custom fuel model support (.flt lookup tables)
→ AMR (adaptive mesh refinement) near the fire front
→ Full 3D spatially-varying wind field input
→ Two-way fire-atmosphere coupling (WRF-AMR interface)
→ Ensemble / Monte Carlo runs with stochastic moisture
→ Live fuel moisture from satellite (NDVI → FMC)
→ Post-frontal smouldering and ember accumulation
→ Real-time assimilation of observed fire perimeters
→ Web dashboard for operational decision support

## Slide 17
Summary & References
What We Built
✔ Open-source, AMReX-based level-set wildfire solver
✔ Multiple fire spread models: Rothermel, Balbi, Cheney-Gould
✔ FARSITE elliptical expansion on Eulerian grid
✔ Real landscape files: binary and ASCII .lcp
✔ Spatial crown layers CBH/CBD/CC from binary LCP
✔ Fuel adjustment .adj + time-varying .fmd moisture
✔ Fire perimeter CSV/GeoJSON + burned area time series
✔ Scott/Albini max spotting table by fuel model
✔ Multi-resolution timing benchmark (CTest)
✔ GPU-accelerated (CUDA/HIP/SYCL), MPI-parallel
✔ github.com/hgopalan/wildfire_levelset
Key References
Rothermel (1972). USDA For. Serv. Res. Pap. INT-115.
Finney (2004). FARSITE. USDA For. Serv. RP RMRS-RP-4.
Richards (1990). Int. J. Wildland Fire 1(2).
Balbi et al. (2009). Combust. Flame 156(12).
Van Wagner (1977). Can. J. For. Res. 7(1).
Albini (1979). USDA For. Serv. GTR INT-56.
Albini (1983). Combust. Sci. Tech. 32(1-4).
Andrews (2018). USDA For. Serv. RMRS-GTR-368.
Byram (1959). In: Forest fire control and use.
Viegas (2004). Int. J. Wildland Fire 13(2).
Scott & Burgan (2005). USDA FS GTR RMRS-153.
Pimont et al. (2009). For. Ecol. Manage. 258(2).
Cheney & Gould (1995). Int. J. Wildland Fire 5(4).
Zhang et al. (2020). AMReX. J. Open Source Softw.