## Slide 1
Wildfire-AMR
GPU-Accelerated Wildfire Front Propagation Framework
🔥 Physics-Based Fire Spread
🌊 Level-Set Propagation
🖥️ GPU-Native AMReX Kernels
🌲 Multi-Model Fire Ecology
AMReX · CUDA · HIP · SYCL · MPI · FARSITE-Compatible
hgopalan/wildfire_levelset · MIT License

## Slide 2
Motivation & Challenge
Why do we need a new wildfire simulation framework?
The Problem
⚡ Climate change → longer fire seasons, higher intensity
🏘️ Growing wildland-urban interface (WUI) at risk
📡 NWP/WRF wind data needs GPU-ready fire models
🔁 Multi-day runs require scalable HPC solvers
🌐 Decision support demands real-time forecasting
Gaps in Existing Tools
❌ FARSITE / FlamMap: serial, CPU-only, closed-source
❌ WRF-SFIRE: no GPU, heavy atmospheric stack required
❌ FIRETEC/QUIC-Fire: full LES, prohibitive for large domains
❌ Single spread model — no physics alternatives
❌ No multi-station IDW weather · no Viegas eruptive model
→ Wildfire-AMR fills all five gaps with an open-source, GPU-native, multi-model solver

## Slide 3
Simulation Workflow
Per-timestep loop — from inputs to plotfile output
1. Setup Inputs
Terrain LCP · fuel database · weather station (.wtr) · wind field (constant / CSV / WRF)
2. Compute ROS
Rothermel / Balbi / Cheney–Gould / FBP … + wind (WAF/MEWS) + slope + moisture damping
3. Huygens Wavelets
Elliptical wavelets at each fire-front vertex (Richards / Catchpole / Wilson / Lemniscate)
4. Propagate Front
Level-set WENO5-Z · FARSITE ellipse · MTT Reinitialization → signed-distance maintained
5. Crown / Spotting
Van Wagner initiation · Cruz active crown ROS Albini 2-D firebrand trajectory + lofting
6. Post-Frontal Burn
Bulk fuel consumption · burnout residence time per fuel model (Rothermel 1983 SAV formula)
7. Write Outputs
Plotfile: φ, ROS, I_B, flame length, scorch emissions, TI/CI, moisture fields, diagnostics
↓ repeat each Δt

## Slide 4
Rothermel (1972) Surface Fire Spread
The foundational empirical fire spread model — FARSITE-compatible
No-wind, no-slope ROS:
R₀ = I_R · ξ / (ρ_b · ε_h · Q_ig)
Reaction intensity:
I_R = Γ' · w_n · h · η_M · η_s
Optimum rxn velocity:
Γ' = Γ_max (β/β_op)^A · exp[A(1−β/β_op)]
Moisture damping:
η_M = max(1 − 2.59r_m + 5.11r_m² − 3.52r_m³, 0)
Wind factor:
φ_w = C (β/β_op)^−E · U^B
Slope factor:
φ_s = 5.275 β^−0.3 tan²(θ)
Combined ROS:
R = R₀ (1 + φ_w + φ_s)
Key Parameters
I_R — reaction intensity (BTU/ft²/min)
ξ — propagating flux ratio
ρ_b — oven-dry bulk density
η_M — moisture damping coefficient
η_s — mineral damping coefficient
φ_w — wind factor (empirical U^B fit)
φ_s — slope factor (tan²θ)
β — fuel packing ratio w₀/(δ·ρ_p)
σ — surface-area-to-volume ratio

## Slide 5
Alternative Fire Spread Models
Plug-in library — select with fire_spread_model parameter
Balbi (2009) Physics-Based
Radiation-balance ROS: R = A(1 + sinα − cosα) where: A = χ σ_m δ_m / (2τ₀B*) — fuel radiative amplitude tanα = U/v_b + tanθ — wind+slope flame tilt v_b = √(g δ_m ΔT/T_a) — buoyancy velocity → First-principles, no empirical wind-factor curve
Cheney–Gould (1995) Grassland Empirical
Piecewise linear in 10-m open wind: R = (0.165 + 0.534·U₁₀) × f_MC × CF (U ≤ 5 km/h) R = (−0.020 + 0.640·U₁₀) × f_MC × CF (U > 5 km/h) f_MC = exp(−0.108 × MC%) — moisture correction CF ∈ [0,1] — curing factor → Calibrated on Australian grassland fires
Cruz et al. (2005) Crown Fire ROS
Active crown spread (continental US): R_c = 11.02 · U₁₀^0.90 · CBD^0.19 · exp(−0.17 · FMC) Passive blend: R = R_s + min(1,TI_ratio) (R_c − R_s) → Switches automatically from surface to crown based on Van Wagner (1977) threshold intensity I₀
Lautenberger (2013) Physics-Based
Thermal ignition model: R = k_f · exp(−E_a / R_g T_i) · Q_f / (ρ_f C_f ΔT) Energy balance accounts for radiation, convection and fuel geometry. → Parameter-rich physics from laboratory calorimetry

## Slide 6
Three Fire Front Propagation Methods
Select with propagation_method = levelset | farsite | mtt
Level-Set (WENO5-Z / RK3)
∂φ/∂t + V|∇φ| = 0
• φ < 0 → burned interior
• φ = 0 → active fire front
• φ > 0 → unburned fuel
WENO5-Z upwind spatial stencil
RK3 time integration
Reinitialization keeps φ as signed-distance
Front merging / islands automatic
No explicit perimeter connectivity needed
FARSITE Huygens Ellipse (Richards 1990)
r(θ) based on fire shape model:
Richards: (a cosθ + b sinθ) R Δt
Catchpole: ab / √(b²cos²θ + a²sin²θ)
Wilson: ℓ / (1 − e cosθ) (conic section)
Lemniscate: [b + (a−c)/2 cosθ] R Δt
Anderson L/W ratio sets a, b, c from wind speed
Wavelet per front vertex → merge to new perimeter
Minimum Travel Time (MTT / Dijkstra)
T_new = T_curr + d_s / R_interface
R_interface = 2·R_a·R_b / (R_a + R_b) (harmonic mean)
φ(i,j,k,t) = T(i,j,k) − t
Dijkstra min-heap → exact for any non-negative ROS
Fast-march runs once; update is trivially parallel
No reinitialization needed
⚠ ROS field frozen at t=0 (no time-varying wind)

## Slide 7
Crown Fire Modelling
Van Wagner initiation → passive blend → Cruz et al. active crown ROS
Crown Fire Physics Pipeline
Step 1 — Initiation Criterion (Van Wagner 1977)
I₀ [kW/m] = 0.010 × CBH × (460 + 25.9 × FMC) If Byram intensity I_B ≥ I₀ → crown fire begins
Step 2 — Active Crown Criterion (Van Wagner 1977)
R'_SA [m/s] = 3.0 / (CBD × 60) If R ≥ R'_SA → fire transitions to active crown spread
Step 3 — Cruz et al. (2005) Active Crown ROS
R_c = 11.02 · U₁₀^0.90 · CBD^0.19 · exp(−0.17·FMC) Calibrated against Canadian and US crown fire data
Step 4 — Passive Crown Blend
TI_ratio = I_B / I₀ (torching ratio) R_blend = R_s + min(1, TI_ratio) × (R_c − R_s)
Step 5 — Rothermel (1991) Multiplier
R_crown = 3.34 × R_surface (continental US) Applied when Cruz model is not active
Scott & Reinhardt (2001) TI / CI Diagnostics
Torching Index (TI)
ratio = I_B / I₀
≥ 1.0 → passive/active crown
Crowning Index (CI)
ratio = R / R'_SA
≥ 1.0 → active crown fire
FMC Seasonal Schedule
Built-in phenology curve:
Winter 85% → Summer 140% → 85%
(S. California chaparral)
Crown Activity Output Field
0 = surface fire
1 = passive crown
2 = active crown

## Slide 8
Firebrand Spotting — Albini (1983) 2-D Trajectory
Physics-based lofting + horizontal wind-advected particle trajectory
Stage 1 — Thermal Lofting Height
Byram fireline intensity: I_B [kW/m] = R · w₀ · h / 60 × 3.459 Lofting height (Albini 1983): H_z [m] = 12.2 · I_B^(1/3) Cells with I_B < I_B,min do not generate firebrands
Stage 2 — 2-D Horizontal Trajectory
Flight time: t_f = H_z / v_t (terminal velocity v_t) Forward Euler sub-steps (n_traj steps): x(t+Δt) = x(t) + u(x,y) · Δt y(t+Δt) = y(t) + v(x,y) · Δt Bilinear interpolation of cell-centred wind field Landing: circular ignition zone radius = spot_radius
Diagnostic Output Fields
albini_Hz — lofting height at source cells
albini_count — firebrands launched per cell
albini_dist — max landing distance
albini_active — cells with spot ignitions
Also available: stochastic probability-based spotting model (log-normal landing distance)
Retardant Suppression
Inside active aerial retardant drop zones: f_ret = 1 − ε · exp(−(t−t_drop) / τ_decay) Both ROS and spotting probability are suppressed by the same factor f_ret — matching FARSITE's aerial retardant model behaviour.

## Slide 9
Terrain, Wind & Heat Flux Effects
Per-cell slope/aspect, wind adjustments, and fire-induced flow corrections
Terrain Slope Effects (Rothermel 1972)
Slope factor:
φ_s = 5.275 β^−0.3 tan²(θ)
tan²(θ) = (∂z/∂x)² + (∂z/∂y)²
Viegas (2004) exponential alternative:
Φ_s,V = exp(a_V · tanφ)
Eruptive regime flag: tanφ > 0.4
LCP provides per-cell elevation,
slope & aspect from FARSITE landscape
Wind Adjustments (Andrews 2018)
Wind Adjustment Factor (WAF):
WAF = 1.83 / ln((20 + 0.36h) / 0.13h)
Converts 20-ft NWP wind → midflame
Max Effective Wind Speed (MEWS):
φ_w,max = 0.9·I_R
Caps ROS at Rothermel calibration range
Multi-station IDW spatial wind:
V_cell = Σ(w_i·V_i) / Σw_i
w_i = d_i^−p (default p=2)
Fire-Induced Wind (Heat Flux Correction)
Upward convective velocity:
w↑ = k↑ √(g·Q·H_ref / ρ·Cp·T_a)
Horizontal inflow (entrainment):
U_ind = k_ind · w↑
directed anti-parallel to ∇φ
Balbi buoyancy augmentation:
v_b,eff = √(v_b,fuel² + v_b,Q²)
Stronger plume → more vertical flame
→ reduced ROS (physically consistent)

## Slide 10
Fuel Moisture & Fire Ecology Diagnostics
Dynamic moisture modelling + per-cell ecological outputs
Fuel Moisture Models
Nelson (2000) Diurnal EMC: Equilibrium moisture from T and RH hourly schedule Precipitation Wetting / Drying (Rothermel 1983): M_new = M_sat(1−e^(−Δt/τ_wet)) + M_old·e^(−Δt/τ_wet) M_new = M_EMC + (M_old−M_EMC)·e^(−Δt/τ_dry) τ_wet: 1-hr=1h / 10-hr=2h / 100-hr=4h Per-cell spatial moisture from FARSITE .fms scenario: 5 components: d1/d10/d100 dead + lh/lw live Stored as MultiFab; GPU-safe device lookup Live Fuel Conditioning Ramp: M_lh → M_d100 × 1.5 (herbaceous) M_lw → M_d100 × 2.0 (woody) Matches FARSITE spin-up behaviour Output: moisture_d1/d10/d100/lh/lw in every plotfile
Fire Ecology & Emissions
Byram (1959) Fireline Intensity:
I_B [kW/m] = H · w_a · R
Flame Length: L_f = 0.0775 · I_B^0.46
Scorch Height (Van Wagner 1973):
H_s = 0.1483 · I_B^(2/3)
Tree Mortality (Ryan & Reinhardt 1988):
CSR = (H_s−CBH)/(H_tree−CBH)
P_kill = 1 / (1 + exp(−4(CSR−0.6)))
50% kill at 60% crown scorch
Fire Emissions (Seiler & Crutzen 1980):
E = W_fuel × f_c × EF_species
CO₂=1.570 / CO=0.102 / PM₂.₅=0.0162 kg/kg
Fire Whirl (Weise & Biging 1996):
Fr = U² / (g·L_f) → tilt, height, radius, Ω

## Slide 11
Novelty & Key Differentiators
What makes Wildfire-AMR unique vs. FARSITE / WRF-SFIRE / FlamMap
🖥️ GPU-Native Kernels
AMReX CUDA / HIP / SYCL throughout. FARSITE, FlamMap, WRF-SFIRE are serial CPU-only.
🔢 Multi-Model Spread Library
7 fire spread models in one solver. FARSITE has only Rothermel (1972).
🌊 Eulerian Level-Set (WENO5-Z)
Automatic merging of fire fronts and islands. No explicit perimeter connectivity management.
🌪️ Viegas Eruptive Fire Diagnostic
Exponential slope factor Φ = exp(a_V tanφ) flags cells where Rothermel under-predicts by ε=(R_V−R_R)/R_R.
🔥 Fire Whirl Characterisation
Weise & Biging (1996) whirl geometry from Byram intensity + Froude number — unique among open-source tools.
📡 Multi-Station IDW Weather
Spatial wind interpolation from multiple .wtr stations. No other open-source tool supports this natively.
🌲 Albini 2-D Trajectory Spotting
Firebrands lofted by Albini (1983) plume formula then advected through full 2-D wind field.
🛡️ Embedded Boundary Support
AMReX EB: buildings and fuel breaks on Cartesian grid without remeshing — unique in this class of solver.

## Slide 12
Comparison with Existing Tools
Wildfire-AMR vs. FARSITE · WRF-SFIRE · FlamMap · FIRETEC
Capability
Wildfire-AMR
FARSITE
WRF-SFIRE
FIRETEC
Surface ROS models
7 (Rothermel+6)
Rothermel only
Rothermel only
Physics LES
Propagation
LS + FARSITE + MTT
Huygens wavelet
Level-set (Euler)
CFD Eulerian
Crown fire
Van Wagner + Cruz + TI/CI
Van Wagner
Van Wagner
Physics comb.
GPU acceleration
✓ CUDA/HIP/SYCL
✗
✗
Partial
MPI parallelism
✓ AMReX MPI
✗ Serial
✓ WRF MPI
✓ MPI/OpenMP
Embedded boundary
✓ AMReX EB
✗
✗
✓ 3-D geom.
Firebrand spotting
Albini 2-D traj.
Albini empirical
Not included
Select vers.
Open source
✓ MIT
✗ Proprietary
✓ WRF
Restricted
Atmo. coupling
Heat-flux corr.
None
Two-way WRF
One-way QUIC

## Slide 13
Summary & Future Directions
A GPU-native, physics-rich, open-source wildfire simulation platform
What Wildfire-AMR Delivers
✓ Unified interface: 7 fire spread models +
3 propagation methods in one framework
✓ GPU kernels (CUDA/HIP/SYCL) via AMReX
— serial tools are orders of magnitude slower
✓ Automatic front merging via level-set φ
— no Huygens connectivity bookkeeping
✓ Full fire ecology pipeline: crown, spotting,
emissions, tree mortality, fire whirls
✓ Dynamic fuel moisture: diurnal, rain wetting,
live conditioning, per-cell .fms spatial data
✓ FARSITE-compatible inputs: LCP, .wtr, .fms,
retardant drops, non-burnable masking
✓ MIT open-source — reproducible science
Future Directions
🔗 Two-way fire–atmosphere coupling
→ ERF (Energy Research & Forecasting)
atmospheric model integration
📐 Adaptive Mesh Refinement (AMR)
→ AMReX AMR infrastructure already in place
→ Refine grid near fire perimeter only
🌏 WRF-driven ensemble fire forecasting
→ Multi-station IDW + WRF wind fields
→ Stochastic spotting ensembles
🛠️ Smoke & air quality coupling
→ CO₂ / CO / PM₂.₅ emission transport
🏙️ Urban wildfire (WUI) simulations
→ Embedded boundary buildings +
→ FARSITE-style fuel mapping in WUI zones
📊 Machine-learning ROS surrogates
→ GPU-trained correction of Rothermel
→ from high-fidelity LES data